Custom Neighborhoods Using the User Connector

    The user connector, a pair of 50-pin male flat cable headers on the upper
right edge of the CAM board (see the Hardware Manual for further details, and
the file PINOUT.DOC) has pins carrying all the neighbor output signals and
table address input lines of CAM.  This makes it possible for the user, with
modest effort, to implement rules depending on other combinations of neighbors
than those allowed by the standard major neighborhoods N/VONN, N/MARG-HV,
N/MARG-PH, and N/MOORE; and standard minor neighborhoods &/PHASES, &/CENTERS,
and &/HV.  Using the user connector, any set of up to 12 neighbor and
pseudoneighbor signals may be used to determine the next state of CAM-A
(planes 0 and 1), while another arbitrary set of up to 12 signals determine
the next state of CAM-B (planes 2 and 3).

    Physically, a custom neighborhood is most easily implemented by
custom-wiring a pair of female flat-cable headers with individual wires
unravelled from standard flat cable.  When these custom-wired female headers
are plugged onto user connector on the CAM board, the desired connections are
established.  The pair of custom-wired female headers can later be unplugged
from the CAM and set aside for subsequent experiments involving the same
custom neighborhood.


The user connector contains four kinds of signal sources that can be used as
neighbors or pseudoneighbors:



    a) The 36 "plane outputs" comprising all Moore neighbors of the four bit
planes, named as indicated by the examples

   N0  = north neighbor on plane 0,
   C2  = center cell on plane 2, and
   SW3 = southwest neighbor on plane 3.

etc.


    b) Four "Phase bits" P0, P1, P2, and P3, which can be read by CAM as
pseudoneighbors PHASE, PHASE', &PHASE, and &PHASE' respectively, and whose
value can be altered between steps by the software using commands such as

   1 IS <PHASE>    (sets P0 to 1)
   0 IS <PHASE'>   (sets P1 to 0)
   2 IS <PHASES>   (sets P1 to 1 and P0 to 0)
   3 IS <&PHASES>  (sets P2 and P3 both to 1)

The important thing to remember about these phase bits is that their value
remains constant for all sites throughout a step.  Some or all of these phase
bits can be accessed through the standard neighborhoods, using the commands
N/MARG-PH and &/PHASES, but their presence on the user connector allows them
to be used in arbitrary combinations with other neighbor signals.


    c) Two "parity bits" HT and VT which give the currently scanned site's
horizontal and vertical address, mod 2, relative to the chosen origin (the
parity of the origin can be changed between steps by commands such as 1 IS
<ORG-HV>, which sets the horizontal origin odd, vertical even).  Like the
phase bits, these parity bits are accessible from some of the standard
neighborhoods (e.g. &/HV), but are put on the user connector to make them
accessible in arbitrary combinations with other signals.


    d) Four plane-edge signals H00, HFF, V00, and VFF, which indicate when the
currently scanned site is in the first or last column or row of the 256-by-256
array.  These signals are "active low" which means that they are 1 most of the
time but assume the value zero under the following conditions

V00 = 0  for sites in row 00 (top edge of screen)
VFF = 0  for sites in row FF (bottom edge of screen)
H00 = 0  for sites in column 00 (left edge of screen)
HFF = 0  for sites in column FF (right edge of screen)

These signals are not part of any of the standard neighborhoods.  They can be
used to provide boundary conditions at the edges (e.g. an absorbing boundary
for diffusing particles), or to modify the wraparound, as is done for example
in the experiments 64KWIDE.EXP and MORE64K.EXP, which use the edge signals to
define a spiral wraparound that turns the 256-by-256 system effectively into a
65536-by-1 site system useful for simulating very large one-dimensional
cellular automata.


      Besides these OUTPUT pins, the user connector contains two kinds of
INPUT pins that are useful in realizing custom rules and neighborhoods.


     The most important input pins on the user connector are the twenty "Table
Address Inputs" used as custom inputs to the tables.  Of these twenty, ten,
designated UA02 through UA11, go to the tables controlling CAM-A and the other
ten (UB02 through UB11) go to the tables controlling CAM-B.

    When standard neighborhoods such as N/MOORE &/CENTERS are in effect the
signals presented to these pins are ignored by CAM, but if N/USER or &/USER is
in effect, they are routed as addresses to the tables.  For more details see
the User's Guide, which also gives details on the Forth word == used to assign
convenient names to the user neighbors.  Useful examples may be found in the
annotated experiment 64KWIDE.EXP and the more advanced MORE64K.EXP, as well
as in Chapter 10 of the User's Guide.


    Besides the table address inputs, the user connector contains four "Plane
Input" pins UI0, UI1, UI2, and UI3, which bypass the internal tables entirely.
Normally signals presented at these pins are ignored, but appropriate commands
such as "EXTERN-A," defined on screen 1 of the file MORE64K.EXP, cause CAM-A,
or CAM-B (or both) to take the new state of the planes from the plane inputs
instead of from the internal tables.

    These plane inputs are used in a fairly trivial way in MORE64K.EXP, to
implement some simple data transfers by simply wiring a plane output to a
plane input.  For example, wiring the plane output S3 to the plane input UI3
causes each site of plane 3 to take its next state from the present state of
its southern neighbor, instead of from the internal CAM-B tables, whenever
EXTERN-B is in effect.

    A more sophisticated and powerful way of using the plane inputs would be
to use active external hardware (e.g.  gates or a clocked RAM look-up table)
to COMPUTE the value to be supplied to the plane input pins.  In this case the
external hardware would be substituting for the internal table, and if it were
complicated enough, could overcome some of the limitations of the internal
table such as the restriction to twelve neighbors.  Of course, in this case
the female headers plugged onto the user connector would not be functioning as
a simple plugboard, but rather as a link to active external hardware, (e.g.
another card) which would require its own power and ground.  The external
hardware would not, however, require its own clock, since the clock signal of
the CAM is already available on the user connector.

    Another, less ambitious but probably equally useful, way of overcoming the
twelve-neighbor limitation would rely on the internal tables, with their limit
of twelve input lines, but would do a small amount of preprocessing of the
available neighbor and pseudoneighbor signals before feeding them in as table
address inputs.  For example, in the experiment 64KWIDE.EXP (which see) the
eastern spiral-wraparound neighbor is computed within the tables from the east
neighbor, northeast neighbor, and the signal HFF, thereby using three address
lines to compute one spiral neighbor.  If this computation were performed
externally, only the result would have to be fed in, saving two address lines.

    The computation (a choice between E and NE under the control of HFF) could
be performed by very simple external hardware consisting of a single
data-selector chip such as 74F157 (in fact, one 74F157 chip could compute
spiral east neighbors on all four bit planes, and another could compute spiral
west neighbors on all bit planes).  The only caution in performing such
preprocessing is the need to avoid delaying the signals too much on their way
to being used as table address inputs.  This can be achieved by using only one
stage of preprocessing logic, using fast chips, and avoiding long wires
between the preprocessing logic and the user connector.  The pair of 74F157
chips would require their own ground and power (+5 volts, obtained from the PC
power supply or bus), and, for good design, their own bypass capacitors, but
otherwise would be scarcely more complicated or bulky than a passive
plug-board type customization of the user connector.